## Slide 1
REVIEW 1
Design, Verification and Performance Evaluation of a Hybrid Mesh–Spidergon Network-on-Chip Architecture
Submitted to: Dr. Deepak CH
By:
Ravi Teja 23BEC7342
John Joyce 23BEC7335
Anirudh 23BEC7217

## Slide 2
Project Background
More IP cores on one chip
▶
Every core must talk to others
▶
Dedicated wires / shared bus
▶
Wiring, congestion, latency
▶
Need structured network: NoC
Modern SoCs integrate tens to hundreds of IP blocks, so on-chip communication, not computation, now limits performance.
A shared bus serializes traffic, so adding cores shrinks the bandwidth each core gets.
Full point-to-point wiring avoids that, but every new IP needs a link to every existing IP, so wires and area grow quickly.
Both fail to scale, which leads to a Network-on-Chip: routers and short links that carry packets between IPs.
A NoC also needs a good topology, which is the question this project answers.

## Slide 3
Problem Statement
The problem
In a flat Mesh NoC, packets between distant cores must cross many routers hop by hop, so latency and congestion grow with chip size. A single large Ring/Spidergon shortens global paths but cannot physically scale to many routers. How can a 64-router NoC keep Mesh regularity for local traffic and still give distant clusters short, direct paths?
More IP cores
▶
Long multi-hop paths and congestion
▶
Neither pure Mesh nor pure Spidergon fits
▶
Hybrid: Mesh clusters + Spidergon-like backbone

## Slide 4
Motivation – Why Hybrid?
Topology | Advantage | Limitation
Bus | Simple | Poor scalability
Ring | Simple global connectivity | Higher latency
Mesh | Regular / scalable | Long global paths
Spidergon | Improved global connectivity | Less suitable as complete local structure
Hybrid | Local regularity + global shortcuts | More complex design

## Slide 5
Objectives
Design a hybrid NoC architecture; divide it into local mesh clusters.
Connect clusters with Spidergon-like global links.
Design a multi-port router with buffering, routing, arbitration and crossbar.
Implement packet routing and verify routing correctness.
Test simultaneous, contention and burst traffic.
Develop performance-measurement infrastructure (latency, hops, throughput).
Compare the hybrid approach against baseline architectures.

## Slide 6
Existing / Related Work
Architecture | Problem it solved | Gap that motivates us
2D Mesh | Regular, easy layout | Long cross-chip paths
Torus | Fewer hops via wrap-around | Long wires, timing issues
Ring / Spidergon | Short global paths (across links) | Poor physical scaling as one big ring
Fat-Tree / Butterfly | High bisection bandwidth | Complex, irregular wiring
Hierarchical / hybrid | Locality + global shortcuts | Our chosen direction
Also surveyed: XY / adaptive routing, round-robin vs fixed vs age-based arbitration, congestion management.
Notes: Add 2-3 paper references here if your guide expects citations.

## Slide 7
Proposed Architecture
4×4 Mesh cluster
16 routers
▶
4 clusters
▶
Spidergon-like
global network
▶
64-router
Hybrid NoC
Parameter | Design
Clusters / mesh size | 4 / 4×4 (16 routers per cluster)
Total routers | 64
Gateway | Router R0 (0,0) of each cluster
Packet width | 48 bits
Router ports | 6 (Local, N, S, E, W, Gateway)

## Slide 8
Hybrid Topology Diagram

## Slide 9
Router Architecture
ROUTER
(6x6 crossbar)
NORTH
SOUTH
WEST
EAST
LOCAL (IP)
GATEWAY
Five local ports: Local, North, South, East, West.
Gateway port: 6th port added to R0 of each cluster for global traffic.
Why: no extra gateway router → zero additional router hardware and no extra hop.

## Slide 10
Packet Format (48 bits)
DC
2b
DR
2b
DCol
2b
SC
2b
SR
2b
SCol
2b
Type
2b
Pri
2b
Payload[31:0]
32 bits (txn ID in metrics)
Destination (cluster/row/col) | Source (cluster/row/col) | Type, Priority | Payload — total 48 bits
Field | Bits | Meaning
Dest cluster / row / col | 2 / 2 / 2 | Target router address
Source cluster / row / col | 2 / 2 / 2 | Origin address
Type, Priority | 2 / 2 | Packet class, arbitration priority
Payload | 32 | Data (later reused as transaction ID by metrics monitor)

## Slide 11
Routing Methodology
Same cluster
XY routing inside the 4×4 mesh.
Source
▶
Gateway R0
▶
Global network
▶
Dest gateway
▶
XY to dest
Different cluster
Go to gateway → cross global link → destination gateway → XY.
Local hops: |Sr−Dr| + |Sc−Dc|
Inter-cluster hops: Sr + Sc + 1 + Dr + Dc

## Slide 12
Design Flow
Architecture
▶
RTL
▶
Module verification
▶
Integration
▶
Simulation
▶
Debugging
▶
System verification
Tools: Verilog HDL, Vivado XSim.

## Slide 13
Expected Contributions
Hybrid Mesh + Spidergon-like topology implementation.
64-router architecture (4 × 4×4 clusters).
Gateway-based inter-cluster communication.
Complete RTL implementation.
Comprehensive verification (exhaustive + stress).
Performance-measurement infrastructure and topology comparison.

## Slide 14
Planning / Timeline
Review | Focus | Status
Review 1 | Problem, literature, architecture, methodology | This review
Review 2 | RTL, integration, functional verification | Planned
Review 3 | Verification recap, metrics, benchmarking, comparison | Planned

## Slide 15
Finalized Idea: the Full NoC
Item | Final decision
Topology | 4 Mesh clusters + Spidergon-like global links
Size | 4 x (4x4) = 64 routers
Gateway | R0 (0,0) of every cluster
Global links | Ring + opposite (C0-C2, C1-C3)
Router | 6 ports, buffers, arbiter, crossbar
Packet | 48 bit, 32-bit payload
Routing | XY local, gateway-directed global
Architecture frozen; RTL implementation starts in Review 2.

## Slide 16
Review 1 – Conclusion
Problem defined: scalable low-hop communication for 64 cores.
Hybrid topology chosen and justified against Bus, Ring, Mesh, Torus, Spidergon.
Full NoC architecture finalized (64 routers, 6-port routers, 48-bit packets, gateway-based routing).
Next: RTL implementation and integration (Review 2).